G. INTERFERENCE POWER PARTITION

There is no “golden rule” for partitioning the interference effects for but a reasonable approach is to split the interference power equally between receiver inter-modulations, local oscillator phase noise and spurious. If receiver selectivity is not excellent it may also be necessary to include the finite selectivity of the receiver filters as well. The interference power, PI, may be partitioned into:

(8)

Where PIntermod is the interference power resulting from inter-modulation of the interfering tones, PSelectivity is the interference power resulting from direct leakage of the 2nd image frequency and PSynth is the interference power resulting from reciprocal mixing.

As stated in previous section, the interference power at the receiver input, which arises from reciprocal mixing, PSynth, shall be not greater than PI. This places a requirement on the 1st local oscillator in terms of spectral purity at interference spacing from the carrier. The phase noise requirements are [12]:

ΦN = -(I + PI) 					(9)

Where:

I = Interference

W= Wished Signal

PI = Interference Power

# CONCLUSIONS

This paper has presented a brief review of RF digital receiver topologies, although there are several open issues and a fair comparison among different topologies requires more research, in this paper it is suggested that high integration tends to select low-IF topology for software radio applications. The RF wireless concepts were considered and an insight was provided to derive the expressions for the calculation of wireless receiver selectivity, sensitivity, inter-modulation, and synthesizer phase noise. The next step for this work is to consider the cascade receiver issues and consider the principal wireless standards.

REFERENCES

[1] 	Cetin, E.; Kale, I., “ Morling, R.C.S., Performance of an adaptive homodyne receiver in the presence of multipath, Rayleigh-fading and time-varying quadrature errors”, Circuits and Systems, 2003. ISCAS '03. Proceedings of the 2003 International Symposium, Volume: 4, 25-28 May 2003, Pages: IV-69 -IV-72 vol.4

[2] 	A.A. Abidi, Direct-Conversion Radio Transceivers for Digital Communications, IEEE Journal of Solid-State Circuits, Vol. 30, pp.1399-1410, December 1995.

[3] 	Farazian, M.; Shoaei, O., Yavari, M, “Topology selection for low-voltage low-power wireless receivers”, Electronics, Circuits and Systems, 2003.

ICECS 2003. Proceedings of the 2003 10th IEEE International Conference, Volume: 1 , 14-17 Dec. 2003, pp:20 -23 Vol.1

[4] 	J.F. Wilson et Al., A Single Chip VHF and UHF Receiver for Radio Paging, IEEE Journal of Solid State Circuits, Vol. 26, pp. 1944-1950, December 1981.

[5] 	M. D. McDonald, “A 2.5 GHz BiCMOS Image Reject Front End”, ISSCC Dig. Tech. Papers, pp. 144-145, February 1993.

[6] 	Leon W. Couch II, “Modern Communication Systems. Principles and Applications”, Prentice Hall.

[7] 	Fuqin Xiong, “Digital Modulation Techniques”, Artech House, USA 2000.

[8] 	TIA/EIA IS-137-A, “TDMA Cellular/PCS – Radio.

[9] 	Razavi, B., ¨RF Microelectronics¨, Prentice hall series 1998.

[10] 	Springer, A.; Maurer, L.; Weigel, R.; “RF system concepts for highly integrated RFICs for W-CDMA mobile radio terminals”; Microwave Theory and Techniques, IEEE Transactions on, Volume: 50, Issue: 1, Jan. 2002

[11]	Mattisson, S.; “Architecture and technology for multistandard transceivers”; Bipolar/BiCMOS Circuits and Technology Meeting, Proceedings of the 2001, 30 Sept.-2 Oct. 2001.

[12] 	Gonzalez, J; Santana, D; Gonzalez, L; Garcia, A; “RF Analysis Applied to Digital Wireless Receivers Design” Accepted IEEE Computer Society Press in the proceedings of the IEEE Computer Society Press 2005.

# Text boxes

Figura 4.  Interferente Power Resulting